## Slide 1
CODE2CREATE 7.0 · HACKATHON SUBMISSION
OPTISERVE-EDGE
Efficient Multi-Agent LLM Inference on Ultra-Constrained Edge Hardware
A1
A2
A3
MULTIPLE SPECIALIZED AGENTS
OPTISERVE-EDGE
LOCAL GPU · < 4 GB VRAM
OPTISERVE-EDGE
1 / 14

## Slide 2
The Problem: AI Agents Break Edge Hardware
Multi-agent workflows generate concurrent inference requests that amplify memory pressure and latency.
PL
Planner
CO
Coder
TE
Tester
DE
Debugger
RE
Reviewer
Concurrent Inference Requests
< 4 GB VRAM
AVAILABLE EDGE GPU MEMORY
MEMORY PRESSURE
QUEUEING
OOM RISK
OPTISERVE-EDGE
2 / 14

## Slide 3
Why Naive Local Inference Breaks
GPU VRAM COMPOSITION
4 GB BUDGET
Overflow — exceeds budget
Model Weights
Agent 1 KV Cache
Agent 2 KV Cache
Agent 3 KV Cache
Runtime / Buffers
HEAD-OF-LINE BLOCKING
LONG REQUEST
QUEUE
OTHER AGENTS WAIT
⏱
⏱
⏱
Idle agents waiting on a single blocked request
Model fits ≠ workload fits.
OPTISERVE-EDGE
3 / 14

## Slide 4
The bottleneck is not just the model.
It is how inference is managed.
WEIGHTS
QUANTIZE
REPEATED PREFIXES
CACHE
CONCURRENT REQUESTS
BATCH
UNCONTROLLED MEMORY
CONTROL
OPTISERVE-EDGE
OPTISERVE-EDGE
4 / 14

## Slide 5
Our Solution: OptiServe-Edge
A system-level inference and resource-management layer for multi-agent workloads.
MULTI-AGENT WORKLOAD
API / REQUEST LAYER
OPTISERVE-EDGE
Request Scheduler
Prefix Cache
Memory-Aware Control
Continuous Batching
INT4 / AWQ LLM
LOCAL GPU
OPTISERVE-EDGE
5 / 14

## Slide 6
Optimization #1: INT4 / AWQ Quantization
Reduce model-weight memory to make local inference practical.
FP16
16-bit / weight
INT4 / AWQ QUANTIZATION
INT4 / AWQ
4-bit / weight
Lower weight memory
More memory headroom
Room for KV cache & runtime
Activation-aware Weight Quantization (AWQ) preserves important weight information while aggressively reducing precision.
AWQ is an established quantization technique — not a contribution of this project.
OPTISERVE-EDGE
6 / 14

## Slide 7
Optimization #2: Automatic Prefix Caching
Compute shared prompt prefixes once. Reuse them across agents.
WITHOUT CACHE
WITH CACHE
A1
Common Prefix
Compute
A2
Common Prefix
Compute Again
A3
Common Prefix
Compute Again
Common Prefix
COMPUTE ONCE
A1
A2
A3
Less redundant prefill computation.
OPTISERVE-EDGE
7 / 14

## Slide 8
Optimization #3: Continuous Batching
Keep the GPU working while requests enter and leave dynamically.
NAIVE / STATIC BATCHING
A
B
C
waiting — idle for B, C
Illustrative timeline — conceptual, not measured data
CONTINUOUS BATCHING
A
B
C
D
Illustrative timeline — conceptual, not measured data
New requests enter while existing requests are still generating.
OPTISERVE-EDGE
8 / 14

## Slide 9
Optimization #4: Memory-Aware Request Control
Prevent uncontrolled VRAM growth through admission control.
NEW REQUEST
MEMORY ESTIMATION
VRAM AVAILABLE?
YES
NO
RUN
QUEUE
GPU VRAM BUDGET
Model Weights
KV Cache
Runtime
SAFETY MARGIN
Admission control keeps memory usage inside a safe, predictable budget.
OPTISERVE-EDGE
9 / 14

## Slide 10
Multi-Agent Workflow
Specialized agents collaborate; every inference call routes through OptiServe-Edge.
USER TASK
PLANNER
CODER
RESEARCHER
TESTER
Concurrent Inference via OptiServe-Edge
DEBUGGER
REVIEWER
FINAL OUTPUT
OPTISERVE-EDGE
10 / 14

## Slide 11
Inside OptiServe-Edge: Request Lifecycle
REQUEST
Call arrives from an agent
1
QUEUE
Waits its turn to be scheduled
2
PREFIX CACHE LOOKUP
Checks for a reusable prefix
3
MEMORY CHECK
Verifies available VRAM headroom
4
SCHEDULER
Assigns request to next batch
5
PREFILL
Processes prompt tokens
6
CONTINUOUS DECODE
Generates tokens dynamically
7
STREAM RESPONSE
Returns tokens to the agent
8
Numbered stages trace a single inference request from arrival to streamed output.
OPTISERVE-EDGE
11 / 14

## Slide 12
Baseline vs OptiServe-Edge
BASELINE
OPTISERVE-EDGE
FP16 / Conventional Model
INT4 / AWQ Quantization
+
+
Repeated Prefix Computation
Automatic Prefix Caching
+
+
Naive Request Handling
Continuous Batching
+
+
Limited Concurrency Control
Memory-Aware Scheduling
High memory pressure
Repeated compute
Queueing
OOM risk
Lower weight memory
Less redundant compute
Better utilization
Controlled memory
OPTISERVE-EDGE
12 / 14

## Slide 13
Experimental Methodology
Isolate → Measure → Compare → Validate
ABLATION PIPELINE
BASELINE
+ INT4 / AWQ
+ PREFIX CACHE
+ BATCHING
+ MEMORY CONTROL
FULL OPTISERVE-EDGE
KEY METRICS TRACKED
GPU VRAM
THROUGHPUT
TTFT
P95 / P99 LATENCY
GPU UTILIZATION
CACHE HIT RATE
OOM EVENTS
Every optimization is evaluated independently before testing the complete system.
OPTISERVE-EDGE
13 / 14

## Slide 14
Impact & Validation Plan
Benchmark results are pending controlled hardware testing.
Throughput vs Concurrent Agents
TARGET
Experimental results pending
Peak VRAM vs Concurrent Agents
TARGET
Experimental results pending
TTFT: With vs Without Prefix Cache
TO BE MEASURED
Experimental results pending
OOM Events Under Stress
TO BE MEASURED
Experimental results pending
LOCAL AI
LOWER HARDWARE REQUIREMENTS
BETTER CONCURRENCY
PREDICTABLE MEMORY
PRACTICAL EDGE DEPLOYMENT
From Bigger Models to Smarter Inference.
OptiServe-Edge makes multi-agent LLM inference more practical on severely constrained local hardware.
OPTISERVE-EDGE
14 / 14